# 2010 Changes

This information is from Eric Van Wyk the designer of these components.

## 2010 Power Distribution Panel

- Red LEDs under any wired Wago connections that have pulled breakers

- Self-resetting fuse (5-10 sec) in the camera return path. The PD now protects itself, the camera, the cRIO, and the router when cross-wired.

- In an extreme situation when shorted a third line of PD defense will kick in. This takes 20-40 minutes of resting unpowered to recover entirely

- A tiny bit of extra power supply conditioning

- PCB is Blue (2009 is Red)

## 2010 Analog Breakout

- PCB is Blue (2009 is Red)

- Significantly improves on the accuracy and the noise of the 2009AB, except in two corner cases not found in FRC. Noise is now well below a single-count on the ADC

- Reverse voltage protection to handle cross-wired input power

- Greatly reduced maximum output current - 2010AB ~0.5 amp / 2009AB ~3 amps

- Added low pass filters, so noise coupled in, e.g. from motors, should be somewhat reduced.

- Limits the usefulness of any analog sensors that operate in the kilohertz plus range

## 2010 Digital Sidecar

- Reverse voltage protection

- PCB is Blue (2009 is Red)