Revision: 1.1
Date: 12/7/2009
Author: Neil Rosenberg, FRC Engineering

Restoration instructions for the 2010 Classmate DS laptop computer.

You need:

- An official FIRST Classmate DS laptop

- The FIRST 2010 DS Restoration USB Key

Note:  Restoring your Classmate DS will wipe the internal drive.  If possible please make a backup copy of all valuable data before proceeding, as this will not be possible afterwards.

Instructions:

- With the Classmate powered OFF, insert the bootable USB Key into an available USB port.  Do not use a USB hub, plug the Key directly into the Classmate.

- Power on the Classmate and when you see the 2Go PC screen, repeatedly press F11 until a small window appears entitled “Please Select Boot Device”.

- Using the cursor keys, select the USB Key.  It will likely be the second item in the list, beginning with USB:xxxx.  Do not select the USB:Generic device, this is not your USB Key.  If two identical looking USB items show up, don’t worry.  Select the first of the two.

- Press Enter and allow the Classmate to boot from the USB Key.  Be patient, it can take a minute or more for wpeinit to finish.

- Follow the on-screen instructions