Limitations/restrictions

- sensors cannot have send and receive on the same line

- DMA has only 1 resource available

- Slot 1, Analog input 8 is reserved for battery voltage feedback

Known Bugs

Relay (one direction only)

Setting the relay to run in "Both Directions" works, but the other choices do not work. http://decibel.ni.com/content/thread/6131?tstart=30 
Solution... open up the "RelaySet.vi" and connect the two "Relay Direction" terminals

Jaguar Speed Controllers

- Can have trouble over-current faulting when spinning a flywheel.

- Can have trouble controlling window motors.

Classmate

Broken retention tab on Ethernet port has been a common problem. The Ethernet port works fine but the cable will not stay in unless you hold it in.

A pigtail cable can be wired or glued in place and used