# Network Troubleshooting

## Background Terminology

Definitions:

- Gateway (Transport layer) – converts from one protocol to another, e.g., TCP/IP, IPX/SPX, or Appletalk

- Router (Network layer) – forwards IP packets from one network to another and supports sub networks and VPNs

- Access Point (Data link layer or Network layer) – base station, like a cell phone tower, but much shorter range. Most access points also contain routers like most home wireless routers or cable modems nowadays.

- Switch/Hub (Data link layer) – directs IP traffic to the right directly-connected device.

- Bridge/Repeater (Data link layer) – simply extends a network by connecting two LAN segments together. Think of it as stretching an Ethernet wire using radio waves.

- Wireless – used by bridges, wireless routers, access points to connect devices to a network

A router has these critical settings:

- IP – Internet Protocol address, acts pretty much like a street address for the mailman.

- DHCP – dynamically assigns IP addresses to laptops and other devices. FRC fields don’t use this.

- Netmask –filters unrelated chatter out, so devices don’t waste time watching the traffic go by.

- Wireless:

  - SSID – public name of a wireless network

  - Security – None is usually fine for FRC purposes at home, but WPA is used on the field

- Routing table – maintained automatically as devices connect to the router. This can cause hiccups when changing an IP address, because the old address can be remembered for a while and that disrupts traffic to the new IP address.

A router acts in several ways:

- A network switch for all the IP devices in direct contact with it, i.e., directly populating it’s routing table. When an IP packet arrives for a directly connected device, then the router knows exactly where it is and just switches it.

- A router forwards IP packets from one network to another. For instance, some packets may be destined for the robot or driver station on the 10.xx.yy.zz network, while others may be headed for the Internet while you’re web browsing on the 192.168.0.0 or any of a large number of networks. The netmask tells the router if it’s supposed to send on the packet or just drop it. That lets the router act as a filter for packets to limit unnecessary traffic.

- As a wireless device, a router acts like an access point (think of a cell phone tower)

## FRC Basics

- FRC uses a bridge on the robot, a field access point, network switches at the alliance stations and in the scorpion case, and Ethernet to connect the Driver Station through to the robot.

- Bridge 10.xx.yy.1  (DLink DAP-1522 default address: 192.168.0.90, WGA600N default address: 192.168.1.250, WET610N default address: 169.254.1.250)

- cRIO 10.xx.yy.2 (set by the cRIO Imaging Tool based on the team number given)

- Optional router 10.xx.yy.4 (WRT610N/WRT160N default address: 192.168.1.1)

- Driver Station Ethernet:10.xx.yy.5 and wireless:10.xx.yy.9 (set automatically by the DS application when team # is entered & driver station starts)

- Camera default address:192.168.0.90, used when connecting to the cRIO FRC I port 2. When connected to the DLink access point/bridge use: 10.xx.yy.11

## Competition Network Setup

The setup at competition is the same for most components. The cRIO and Classmate keep their IP settings unchanged. No DS router is used. The wireless DLink on the robot however does get some special settings.

The competition settings for the DLink are changed automatically at a special computer kiosk at each event, but the settings can also be made by hand.

- Mode switch set to Bridge for competition

- Security mode: WPA

- Password: a unique # assigned to each team by FMS

The basic network topology is:

  - Classmate wired to field alliance switch

  - Alliance switches (red/blue) wired to Field Access Point router

  - FMS server also wired to Field Access Point router

  - Field router wireless to robot bridge

  - Bridge wired to cRIO

## At-Home Network Setup

There are many variations, but here are the basics.

The general network topology is:

- Standard

  - Classmate wireless to DLink in AP mode on robot

  - AP wired to cRIO

- Closer to competition

  - Classmate wired to router

  - Router wireless to bridge

  - Bridge wired to cRIO

- Variations

  - Wireless Classmate to router

  - Router replacing bridge on robot and wireless to Classmate

  - Classmate tethered by wire directly to cRIO

## Bridge Default IP

If you have a 2009/2010 WGA600N, then the default address is 192.168.1.250
If you have a replacement WET610N, then the default address is 169.254.1.250

The 2011 DAP-1522 default address is: 192.168.1.50
Otherwise, you setup the FRC IP address the same, i.e., 10.xx.yy.1

## Router-Bridge Setup

If browser pages appear incomplete it is often due to a browser conflict.

Try a different web browser.

## Multiple PC network cards:

National Instruments software uses the system default network card to detect and connect to real-time devices and other remote targets. If you have multiple network adapters, it is possible that the secondary network adapter is searching for the targets. You might want to disable the ports you aren’t using. There are several things you can do:

- Connect your device to the default Ethernet card

- Change the Ethernet port connected to the real-time target to be the default

- Go through the following steps to switch the port you are currently using:

  - Quit the DS application

  - Set all your IP addresses to DHCP or something that’s NOT 10.xx.yy.5

  - Edit the DS .ini file -  c:\Documents and Settings\All Users\Shared Documents\FRC DS Data Storage.ini

  - Change NICNAME=””Local Area Connection”” to the name of your new port.

  - WifiNICName=””Wireless Network Connection”” to the name of your wireless port if you want to use that.

  - Save & quit your text editor

  - Start the DS application

## Cannot Connect to FMS While Using a Remote Dashboard

You cannot connect to the FMS with a bridged connection and another computer hanging off of it on the same 10.xx.yy.z subnet.

## Remote Dashboard

The full FMS blocks all hosts on the 10.0.0.0 network except the FMS server, Field Router, and the six active teams: 10.xx.yy.1 (bridge), 10.xx.yy.2 (cRIO) and 10.xx.yy.5 (Classmate). However, at home or under FMS Light control, forwarding works fine.

If you want to run a 2nd laptop as a remote dashboard in official competition you must use a different IP scheme, e.g.,

- 2nd Classmate Ethernet port: 164.0.0.5

- 2nd laptop: 164.0.0.6

If you don’t need to forward video you can then set the DS to use a Remote Dashboard and give it the 2nd laptop address. If you need video you can use a forwarding proxy installed in place of the classmate's local dashboard or you can modify a dashboard project to use the DS screen for some things, and forward all the information including video on to other laptops.

## Network Security

Make sure all network security settings are common between your PC, router, and bridge, including if automatic Wi-Fi Protected Setup is enabled. The 2009/2010 bridge has a security button that, when pressed or jostled disables it by putting it into Wi-Fi Protected Setup.

Firewalls can block communication, too.

## After a Competition

The robot bridge will have the competition security settings that need to be disabled.

1) Flip the DLink mode switch to AP

2) Tether the Classmate directly to the robot bridge and browse to http://10.xx.yy.1

3) The username & password are: root/blank

4) Browse to Setup->Wireless

5) Use the manual setup and go through the steps to assign your own made-up WPA passcode

6) Switch to wireless and connect. It should appear as a network with your team number. Give it the same WPA passcode as in #5

7) The Driver Station app will need to be switched to use the wireless connection instead of the Ethernet port on the Setup tab or by modifying the .ini file as described earlier.

## Link between the bridge and the cRIO

There is an issue with some setups where the bridge and the cRIO fail to find each other when they are first powered up. Both devices end up waiting for the other to make the first move with the result that no one talks first. Reset the cRIO to fix it, or repower just the bridge. Do not just cycle the power on the robot.

Another fix is running "arp -d" on the classmate to clear the arp cache.

## Cross-over Cables

There are several devices in the control system that require either the use of a cross-over Ethernet cable or a connected device (e.g., laptop) that is auto-sensing. A cross-over cable will also work as well as a regular cable with all auto-sensing devices.

- cRIO

- Axis 206 Camera (not the M1011 replacement camera which is auto-sensing)

The DLink is auto-sensing so its connection to the cRIO can use a regular cable. The Classmate is also auto-sensing so it can be directly connected to the cRIO or directly to the KOP camera with a regular Ethernet cable too. However, not all personal laptops are auto-sensing, so connecting a private PC directly to the cRIO may require a cross-over Ethernet cable to work correctly. A non-auto-sensing PC can use an intermediate router (all routers are auto-sensing) that is then connected to the cRIO to side-step this issue.

The KOP Camera must be connected to the cRIO with a cross-over cable, because neither one of those devices will auto-sense. The camera can be connected directly to an auto-sensing PC, but must use a cross-over cable with any non-auto-sensing PCs.

If the incorrect cable is used then the Ethernet status light on the connection at either end will not light.

## What’s the Difference Between DHCP & Static IP Addresses?

For the critical robot functions, FRC uses static or fixed IP addresses. They are the same for each of the devices no matter where you compete.

DHCP allows IP addresses to be assigned dynamically and is used to allow unlimited extra computers to connect to your network. DHCP is only possible if you have a DHCP server to assign free addresses, i.e., a router.

## Troubleshooting Steps:

Verify your project is using the correct IP address for the cRIO target (10.xx.yy.2). The IP address is displayed in the LabVIEW Project Explorer window as: RT CompactRIO Target (10.xx.yy.02). If it is not correct you can fix it with a right click to get Properties.


Verify your communications:
Does Enabling the Driver Station give you a solid status light on the cRIO's Digital Sidecar? And does Disabling the DS make the Digital Sidecar status light blink? 


Check your PC:
Verify the PC's IP address (10.xx.yy.6), Subnet mask(255.0.0.0), and Default gateway(10.xx.yy.4) are as they should be.
Disable any PC firewall.
Disable any wireless network card.
Test communications to the cRIO by: 
-- Start -> Run
-- then type cmd and OK
-- then in the window that pops-up type: ping 10.xx.yy.2
If you get a message "Request timed out." then your PC truly cannot see the cRIO.

## Connectivity Issues:

- Is your robot attempting to use the wireless bridge for the first time since competition?
The bridge gets a special setup at competition that will prevent it from working at home.
The DLink needs to be reset to work at home:

- Switch the DLink mode switch to AP

- Cable your PC/Classmate directly to the bridge and browsing to http://10.xx.yy.1

- Note: the PC you use must have a compatible IP address such as 10.xx.yy.5 (Classmate default)

- Go to Setup->Wireless

- Choose the Manual setup option, but leave most of the fields as they are.

- Turn the Security off or change it to WPA

- If using security then add a passcode that you make up, e.g., FRCteamxxyy

- Connection is intermittent via wireless to the bridge

If you have other wireless in the area that might be causing conflicts, you will be better off setting the router to a specific channel that is far away from other wireless networks, rather than using the default “auto” channel selection setting. Channels 1, 6, or 11 are recommended.

- Wireless network performance will be greatest when each of the devices on the wireless network are using 802.11n. If an older device using 802.11g or 802.11b connects to your 802.11n-based router, the speed and data rate of all the devices on the network will decrease. One way to get around this issue is to use a dual-band router or access point. This allows older devices to run over one frequency band (2.4 GHz) and newer 802.11n-based devices to use the other frequency band (5 GHz).

- On the driver station Diagnostics Tab a robot light green but robot communication red, indicates the network is fine, but the libraries on the cRIO are not responding. Often caused by mis-matched versions of cRIO image/laptop LabVIEW Update. Could also be that the cRIO DIP switches for Safe or No App modes are set.

- The "Communications" indicator on the driver station flashes from green to red to green, and driver station commands to the robot are delayed, sometimes by a couple of seconds. At home this indicates intermittent communications. Several possibilities include:

  - Cause:

    - 2.4GHz wireless band is saturated by other local network devices utilizing the same frequency

    - Poor robot radio placement

    - Overloaded cRIO

  - Test by switching to Ethernet cables instead of wireless to localize the issue as a true wireless problem. Then isolate the point in the network where the problem arises.

  - Solutions:

    - The DLink can be set to use a different channel. Try different ones to see if it helps.

    - Can test with the alternate 5GHz network if a 5GHz bridge is available or a laptop that supports the 5GHz band for the PC side.

- Robot loses communication while driving

  - Cause: 1) Wireless bridge antenna is too close to metal, buried in the robot, or too close to a speed controller or powerful motor magnetic field

2) Loose Ethernet cables

3) Loose power connector

  - Test:

- Check your network configuration:

  - Check all your cables and make sure they are connected.

  - As a precaution connect your PC directly to the cRIO using a cross-over cable.

  - If this is not possible, try connecting to it through your router using straight through cables.

  - Use the Wireless setup as the last means of communication when troubleshooting connection issues.

  - Ensure that you are using Port 1 on the cRIO for talking to your PC and Port 2 for the Camera.

- Verify that the IP address and Subnet Mask is correct on your PC.

  - The Classmate should be 10.xx.yy.5 and any other PC should be 10.xx.yy.6.

  - The Subnet should be 255.0.0.0

- Disable any software that might prohibit network communication:

  - Disable the Windows firewall by going to Start»Settings»Control Panel»Windows Firewall and click the OFF radio button.

  - Disable any other firewall software.

  - Disable any virus scanning Software.

- If you have more than one network adaptor (Wireless Adaptor and LAN adaptor) than National Instruments software uses the system default network card to detect and connect to real-time devices and other remote targets

  - Go to Start»Settings»Control Panel»Network Connections»Advanced»Advanced Settings...

  - In the list of connections, use the Up and Down Arrows to move the Local Area Connection to the top of the list.

- Disable your Wireless Card by going to Start»Settings»Control Panel»Network Connections and right click on the wireless adaptor and select Disable.

Try resetting the cRIO's IP address by switching the IP Reset Switch to the On position and rebooting the cRIO. This restores the controller to the default IP address (0.0.0.0) or link-local depending on which version of the cRIO Image is currently installed.

If the cRIO-FRC is not able to communicate with the network, you can use the IP RESET switch to manually restore the chassis to the factory network settings (set the DIP switch ON, reset the cRIO, then set the switch back to OFF afterwards). When you restore the chassis to the factory network settings, the IP address, subnet mask, DNS address, gateway, and Time Server IP are set to 0.0.0.0.

When trying to reimage the cRIO:

Unable to complete operation because of unexpected error:
Error 63 occurred at TCP Open Connection in NI_InternetTK_FTP_VIs.lvlib:FTP Open Session.vi->NI_InternetTK_FTP_VIs.lvlib:FTP Get Multiple Files and Buffers.vi->NI_InternetTK_FTP_VIs.lvlib:FTP Get File.vi->ConfigUtility.lvlib:OpenRemoteConfiguration.vi->ConfigUtility.lvlib:ReImageTarget.vi->ConfigUtility.lvlib:Dialog.vi

Possible reason(s):

LabVIEW: Serial port receive buffer overflow.
=========================
LabVIEW: The network connection was refused by the server. For TCP/IP, make sure the server is running and listening on the port you are trying to use. Firewalls can also cause a server to refuse a connection. For VI Server, make sure you have enabled VI Server from Tools>>Options>>VI Server:Configuration.

Troubleshooting:

Turn off firewalls and all other network interfaces.

Probably turn off wireless and connect with a cable to be on the safe-side. Sometimes hooking up directly works, while other situations are helped by connecting through an intermediate router. 

The cRIO Imaging Tool broadcasts to locate cRIOs. Then the Tool communicates with the cRIO to download the image and order the cRIO to reboot. The cRIO then gets a different generic DHCP IP address (in 2009/2010 it was always 0.0.0.0). The computer must then reacquire the re-IP’ed cRIO. This process of searching for the cRIO again may happen faster than the cRIO and network change can respond. The cRIO Imaging Tool must be able to find the cRIO again to complete it’s configuration (network setup, name, ftp the image, etc. It has many steps each of which can fail due to timing conditions associated with the changes in the cRIO’s network address. Contributing to these potential timing windows where communication can fail, are: firewalls, computer drivers, security settings, routing tables/cache, NIC configurations, etc.

Classmate Driver Station Wireless

- Operates at 2.4GHz, so make sure the DLink is setup to receive that.

- Other laptops may use a different frequency

## Network Troubleshooting

DLink  DAP-1522 – 2011 (http://www.dlink.com/products/?pid=663)

Check the Statistics page for TX/RX packet loss on both the wireless connection and the wired Ethernet connections.

That will help identify noise wireless environments or bad radio placement as well as bad Ethernet cable connections.

WGA600N – 2009 (http://homesupport.cisco.com/en-US/wireless/lbc/WGA600N/vRegUrl)

|  | Status -> Statistics gives you some troubleshooting information after the robot has been run awhile. In competition try to examine these statistics BEFORE shutting off your robot after a match. |
| --- | --- |
|  | LAN Statistics This is the wired Ethernet connection to your cRIO TX/RX Packets Dropped indicate a bad cable or bad connectors Wireless Statistics TX/RX Packets Dropped indicate an obstructed bridge antenna |
|  | Tools -> System Check Has a ping test you can use to determine directly if the bridge can see the cRIO. |

## Recommended Default Settings

Variations of these settings can be used if you know what you are doing and what the impact of changes are. These are just suggested settings to get it all working at home. At competition (off-season or official) the bridge settings will be made over based on how the field is setup.

### Robot Bridge

(WGA600N-2009)

|  | Basic -> Network Settings Static IP address IP Address: 10.xx.yy.1 xx.yy = 4 digit team number Subnet Mask: 255.0.0.0 |
| --- | --- |
|  | Basic -> Wireless Wireless Bridge Wireless Network Name (SSID) |
|  | Basic -> Wireless Security Mode: None Note you can add security for use at home |

### Robot Bridge (WET610N – 2010 recommended replacement)

### (http://homesupport.cisco.com/en-us/wireless/lbc/WET610N)

|  | Setup Static IP Static IP Address: 10.xx.yy.1 Subnet Mask: 255.0.0.0 |
| --- | --- |
|  | Wireless Network Name (SSID): Team number Security Mode: Disabled |

KOP Routers

(WRT610N – 2009) (http://homesupport.cisco.com/en-us/wireless/lbc/WRT610N)

(WRT160N- 2010) (http://homesupport.cisco.com/en-us/wireless/lbc/WRT160N)