## Slide 1: FIRST ROBOTICS: Design Strategy
Nolan Conway
Webb Institute
11/22/14

## Slide 2: First Games
Main objective is to score points
Usually there are too many tasks for a single robot to complete on its own
Usually 2 minutes
(time is a problem)

## Slide 3: 5 Simple Steps to Design
1: Know the game
2: Know your limits
3: Pick your part
4: Make tradeoffs
5: Work the details

## Slide 4: Step 1: Know the game
Read the Rules
  Read them again
Look at every method of scoring
  Even the crazy ones Freshmen come up with
Look at all means of defense
Run practice matches in your mind
Develop strategies then look to defend them
Ask how commonly will each strategy be played?

## Slide 5: The Easy Win
A “Chokehold Strategy”
  A strategy that will always end in winning independent of your opponent
FIRST does not like this
  Look out for the Q & A or rule updates

## Slide 6: Step Two: Know Your Limits
Every Team has them!
  Space
  Build time
  Machinery/ Tools
  Knowledge
  Cost
Simpler is
Better

## Slide 7: Step 3: “Pick Your Part”
Prior to this you should know:
  The other robot types that will exist
  The rules……all of them
  What is worth doing
Prioritize
  Scoring, defense, the middle-man, end game
Remember: You are an alliance
  You can rely on the other robots to do some things
  You cannot guarantee an alliance

## Slide 8: For What it is Worth….
Is a task worth the reward for accomplishing it?
You want an easy task that scores big points
How long will it take?
  3 seconds to score a 1-point basket or….
  30 seconds to score a 5-point bonus
Defense is just as rewarding
  10 points kept out are the same as 10 points in
How much weight is dedicated to a single task?
Know the ranking system!

## Slide 9: Step 4: “Make Tradeoffs”
The robot has limits
Your analysis should help you with this
Speed vs. Power
Complexity vs. Durability
Motor Placement
Notes:   To build one item may leave no room for the next

## Slide 10: Step 5: “The Details”
Decide on a drive train
Think of materials
Begin to sketch and draw your design
Get on the same page!
  Brief the whole team

## Slide 11: Drive Train Selection
Choose a system that matches your strategy
Think of your programmers, and drivers
Mobility
Weight
Drivability
Calculate expected speed

## Slide 12: Tank Drive
2, 4, 6, 8 wheel drive
West coast (cantilevered wheels)
Offset center wheel
Speed guidelines:
  3 ft/s: Pushing
  4-7 ft/s: slow/pushing
  8-12 ft/s: quick with some push
  13+ ft/s: very fast, hard control

## Slide 13: Mecanum
71% of Power in primary
50% Perpendicular
Easy to program
Expensive/heavy
Notes: Sqrt(2)

## Slide 14: Holonomic (Omni)
Harder to program
Same power as mecanum
Higher efficiency
No resistance to push
Notes: Less mass to rotate

## Slide 15: Swerve
Requires independent motors
Save motors with crab drive
Very strong pushing
A lot of programing
Pneumatic option
Notes: Some teams combine two sets of wheels. Less motors (crab drive)

## Slide 16: Slide
You will be pushed
Direction is simple summation of movements
Smooth movement anywhere you want

## Slide 17: Butterfly
Pneumatics required
Large maneuvering wheel
Small traction wheel
Combine any two drive trains

## Slide 18: In Practice
Brainstorm
Prototype
  Try what you don’t already know
Decide on a plan
Order Material
Create a detailed design
Build!
Notes:   Use your resources (Chief Delphi)

## Slide 19: Wiggle Room
Leave a little bit of it…
If the maximum width is 26 inches, make the robot 24 inches
  You may need extra space for new mechanisms
  You must fit in the size-box at competition
Leave your self some spare weight
  All scales are a bit different (look at tolerances)
  You may need to add bolts or even whole pieces
  No one likes a cheese-hole robot

## Slide 20: Materials
Things sell out
  Be careful with Andy-Mark
  Robotics-specific items sell out very fast
Look for donations of scrap metal
Keep things Standard (1/4-20)

## Slide 21: Design Tips
Avoid shoulders, grooves or features on active shafts
Set screws do not transfer load!
Chain vs. belt
  Belt saves 2-lbs for 6-wheel drive
  Same stretch, belt is 2% more efficient
Gears trade speed for torque (cant get both)
Shift weight from center
Wheel size should be a big choice

## Slide 22: Hex Drive or Standard
One or the other!
Requires a hex broach to switch ($235)
Lower stress concentrations then keyway
Easier to assemble
Live verse dead axel
Reduces chance of shaft twisting

## Slide 23: Practice Field
Build one…..
  Or at least pieces of it
Wood is quick, cheap, and easy
Build it right!
Use it for prototyping and driver practice
Notes:   For practice field: No point if dimensions are wrong

## Slide 24: Drive, Drive, Drive!
Experience is essential for drivers
Drive a similar robot if available
Practice turns, corners, & fine-maneuvering
Teams that do two regionals have an edge
Practice driving with a coach

## Slide 25: The Cool Factor
Make your robot “POP”
Decorations are important
Clean construction Autonomous movement
A bright color or stand out feature
All of these will help you be scouted!

## Slide 26: Inspect Your Robot
Print the inspection sheet from the FIRST website and USE IT!
From inspections last year:
  Wire size (check the CIMs)
  Have bumpers ready
  Be inside the bumper-zone
  Bumper zone (height/ gaps)

## Slide 27: Say Goodbye
Almost time to relax but…
Take Measurements
  Helpful if you need to make changes
  Be smart about your with-holding allowance
Take a lot of reference photos
Put the bumpers on the robot
Be careful with your Bag….it may tear!
Take a break and relax once it is done

## Slide 28: More Information
Chief Delphi- white papers
www.Simbotics.org
www.team358.org
Email: nconway15@webb.edu