## Slide 1
These introduce only a few of the many variations that are possible with our robot IP networks

## Slide 2
There is Only One Right Way to Setup Our Robot IP Network
Netmask & Other Settings Can Only Be One Way
The Router Doesn’t Remember Past IP Address’s That Have Been Changed
The Router IP Must Be in the Range 10.x.y.z
Our Small Robot Network is Complicated
Wireless and Wired Networks Cannot Be Mixed
Gateway Matters
Wireless security is necessary
There Isn’t a Way to Use DHCP for Every Device in Our Robot Network
The following are just examples of topologies that work, there is a lot of leeway.
Most settings described are only conventions, making it common for all of us
and easier to work with and talk about.
There are many ways to setup our networks that will work.
There are incorrect settings and mixtures of devices that can disrupt everything.
There are only a few must have settings.
A huge variety of IP settings will work, but consistency is a good idea.
Most netmask settings will work for our purposes. You just have to have one. The
least problematical is 255.0.0.0
In the following examples, settings are given if there is a convention for them, but
are often left out if they do not matter.
Noisy wireless areas may need special massaging to make work.

## Slide 3
Private & Public IP networks do not mix, but can share
IP/mask must be compatible between devices that want to talk explicitly to one another, e.g., DS -> cRIO, but not DS->router (We’re talking through the router, not to the router)
Wireless is via a common SSID
Only some IPs must be exactly as stated
  IP is only restricted for the cRIO & Driver Station
  Conventions are: .1=bridge, .2=cRIO, .4=router, .5=DS Ethernet/.9=DS wireless, .11 to .20=camera, .21+=available for DHCP
  Using other IPs will not show in the DS ping display
  DHCP can be used with any router configuration. A dynamic IP is a problem if you need to address a specific device.
  In general, the best netmask for our purposes is 255.0.0.0
Wireless/wired can be mixed
Any bridge or AP device can be used for the robot
Wireless bands and channels must match
Interference from lots of SSIDs can cause packet loss and delay-resulting in jerky robot response.

## Slide 4
What’s Important
IP Network
  The FRC robot network is based on static IP addresses 10.te.am.x
  IPs/netmasks must be compatible between any two devices that want to talk
    Laptop to cRIO example (both these will work)
      Laptop 10.3.58.5/255.0.0.0 -> cRIO 10.3.58.2/255.0.0.0 (good)
      Laptop 10.3.58.5/255.255.255.0 -> cRIO 10.3.58.2/255.255.255.0 (good)
    Laptop to router just to change router settings
      Laptop 10.3.58.5/255.0.0.0 -> router 10.0.100.4/255.0.0.0 (good)
      Laptop 10.3.58.5/255.255.255.0 X-> router 10.0.100.4/255.0.0.0 (bad)
  Routers do NOT need compatible IPs/netmasks just to pass network traffic through
Wireless
  SSIDs must match at both ends (AP <-> robot, laptop <-> AP)
  Security must match at both ends (none, WPA-passcode, etc)

## Slide 5
Blue Alliance
Driver Stations
Red Alliance
Driver Stations
FMS IP: 10.0.100.5
Team DS IP: 10.xx.yy.5
Subnet: 255.0.0.0
User login: Driver
Robot IP: 10.xx.yy.1
SSID: team#
WPA2 security code
Bridge mode
Field Access Point IP: 10.0.100.4
VPN SSID is unique for each team
Managed Switch
Managed Switch
Managed Switch/VPN

## Slide 6
Blue Alliance
Driver Stations
Red Alliance
Driver Stations
FMS Light IP: 10.0.0.5
Subnet: 255.0.0.0
Team DS IP: 10.xx.yy.5
Subnet: 255.0.0.0
User login: Driver
Robot IP: 10.xx.yy.1
Subnet: 255.0.0.0
SSID: event
Bridge mode
Field router IP: 10.0.0.4
Subnet: 255.255.255.0
SSID: event

## Slide 7
IP: 10.xx.yy.5
Subnet: 255.255.255.0
SSID: team# or other uniqueID
Robot IP: 10.xx.yy.1
Subnet: 255.0.0.0
SSID: team# or other uniqueID
AP mode
IP: 10.xx.yy.5
Subnet: 255.0.0.0
Robot IP: 10.xx.yy.1
Subnet: 255.0.0.0
SSID: team#
Bridge mode
Wireless router IP: 10.xx.yy.4
Subnet: 255.255.255.0
SSID: team#
IP: 10.xx.yy.5
Robot IP: 10.xx.yy.1
For multiple wireless robots
use unique SSIDs

## Slide 8
Subnet: 255.0.0.0
Subnet: 255.0.0.0
SSID: team#
Bridge mode
Field router IP: 10.0.0.4
Subnet: 255.255.255.0
SSID: team#
Notes:
With a shared router we need unique team numbers
DS can be wired or wireless
Robot IP: 10.xx.yb.1
Robot IP: 10.xx.yy.1
Robot IP: 10.xx.ya.1
DS IP: 10.xx.yb.9
DS IP: 10.xx.yy.9
DS IP: 10.xx.ya.9
Subnet: 255.0.0.0
Subnet: 255.0.0.0
SSID: team#
Bridge mode
Field router IP: 10.0.0.4
Subnet: 255.255.255.0
SSID: team#
Robot IP: 10.xx.yb.1
Robot IP: 10.xx.yy.1
Robot IP: 10.xx.ya.1
DS IP: 10.xx.yb.5
DS IP: 10.xx.yy.5
DS IP: 10.xx.ya.5
Notes: <number>

## Slide 9
?
IP: 10.xx.yy.11 to .20
Camera login: FRC/FRC
?
?
Default IP: 192.168.0.90
Camera login: FRC/FRC
IP: 192.168.0.zz
?
Axis 206
Requires
X-over cable
Default IP: 10.0.0.10
IP devices are not limited to cameras.
Just no non-KOP wireless devices.

## Slide 10
Subnet: 255.0.0.0
Subnet: 255.0.0.0
SSID: team#
Bridge mode
Field router IP: 10.0.0.4
Subnet: 255.255.255.0
SSID: team#
Robot IP: 10.xx.yb.1
Robot IP: 10.xx.yy.1
Robot IP: 10.xx.ya.1
DS IP: 10.xx.yb.9
DS IP: 10.xx.yy.9
DS IP: 10.xx.ya.9
2009/10 KOP Bridge
2010 Replacement Bridge
2011 KOP Bridge/AP
802.11 supported
2009/10 are n-only
2011 Dlink is a/b/g/n
2009/10 is a/b/g/n, 2.4&5GHz
2010 is b/g/n, 2.4GHz-only
Classmate is b/g device
So cannot talk wirelessly
directly to the older
n-only devices
Make sure your wireless
devices are compatible
Notes: <number>

## Slide 11
Notes:
Common SSID
Unique team numbers for DS/robot pairs
One DLink acts as a central AP router and must be present and powered for all robots to work
Subnet: 255.0.0.0
SSID: xxyy
Subnet: 255.0.0.0
SSID: xxyy
AP mode
Robot IP: 10.xx.yb.1
Robot IP: 10.xx.yy.1
Robot IP: 10.xx.ya.1
DS IP: 10.xx.yb.9
DS IP: 10.xx.yy.9
DS IP: 10.xx.ya.9
Subnet: 255.0.0.0
SSID: xxyy
Bridge mode
Subnet: 255.0.0.0
SSID: xxyy
Bridge mode
Notes: <number>

## Slide 12
Single Robot Independent IP networks –
      Good: for traveling/demo robots, all one team number
      Bad: too many can cause interference, multiple SSIDs, development PCs must change networks
Multiple Robot Integrated IP networks –
      Good: for events, use at home, and with support computers/networks, e.g., development PCs, configuration management system. Less potential for network interference across multiple wireless systems & easier to monitor.
      Bad: not as easily portable, requires more network components/more power plugs

## Slide 13
IP: 10.xx.yy.5
Robot IP: 10.xx.yy.1
Subnet: 255.0.0.0
SSID: team#
AP mode
Standard Public Network
DHCP Server
IP: DHCP
By convention IP addresses that start with 10. are private, meaning that devices outside the immediate network are not allowed to "see" or communicate directly with them.
This precludes direct use of the Internet.
Mixing two networks just requires separate Network Interface Cards (NIC), typically Ethernet & wireless and connections to the individual networks:
One set to a private network address
One set to a public IP, typically using DHCP
DS & Development PC

## Slide 14
IP: 10.xx.yy.5
Wireless IP: DHCP
Robot IP: 10.xx.yy.1
Subnet: 255.0.0.0
SSID: team#
Bridge mode
SSID: team#
IP: 192.168.0.4
Disable DHCP service
IP: DHCP
The router IP does not have to be in the 10.x.y.z range.
The value chosen here is somewhat arbitrary.
In this configuration it will route public LAN & Internet traffic.
Disable the DHCP server settings in the router, because
the Internet router is usually already set to supply this service.
Robot network traffic does not go
to the Internet
Internet Access Point
DHCP Server
Development PC
DS & Development PC

## Slide 15
Used on the FRC field and sometimes at home
Can be setup to use DHCP for ALL devices with required static IPs reserved to specific MAC addresses
A router maintains a table of known IPs/netmasks of devices that have spoken up, describing the topology of the network immediately surrounding it.
  When you change a device to a new IP, packets may not be routed correctly until the old address ages out.
  IP entries age out when updates are not received for some period of time. That time differs by manufacturer.
For devices listed in the routing table the router acts as a simple switch.
“Routing” only occurs between different networks. Traffic on a single network is switched.
The router’s personal IP/netmask is only for talking directly to the router, e.g., logging on. It does not affect other packet routings. The routing table IP/netmasks are used for that.

## Slide 16
Driver Station 1
10.12.34.5
255.255.255.0
Driver Station 2
10.43.21.5
255.0.0.0
Router
10.0.100.4
255.255.255.0
Routing Table
10.12.34.5/255.255.255.0 (DS)
10.12.34.1/255.255.255.0 (Bridge)
10.12.34.2/255.255.255.0 (cRIO)
10.43.21.5/255.0.0.0 (DS)
10.43.21.1/255.255.255.0 (Bridge)
10.43.21.2/255.255.255.0 (cRIO)
Robot Bridge
10.12.34.1
255.255.255.0
Robot Bridge
10.43.21.1
255.255.255.0
cRIO
10.12.34.2
255.255.255.0
cRIO
10.43.21.2
255.255.255.0
The Driver Stations cannot log directly into the router

## Slide 17
Packet – a message from one device to another
Router – packets crossing networks, within a network a router acts as a Switch
Switch – simple forwarding of packets
Access Point – a “router” for wireless packets
Bridge – same network, just extends distance. Wireless bridges generally talk only to access points.
IP - Internet Protocol is the primary Internet addressing scheme
Netmask – isolates sub-nets within a network.
Gateway – a router that also translates between routing protocols like IP or Appletalk. Usually at the edge of a network it often hosts the network firewall. A default gateway is used to send any packets destined for an IP network not explicitly defined in the routing table.
SSID – Service Set Identifier, name of a wireless network
DHCP – Dynamic Host Configuration Protocol, temporary IP addresses assigned automatically by a DHCP server. Some static IPs can be reserved.
Static Routing – permanent IP addresses explicitly assigned.
VPN – Virtual Private Network, secure communications between specific devices. Used in FRC competition to isolate team traffic from one another.
MAC – Media Access Control, a unique id given to every network card in the world

## Slide 18
Diagnostics Available to Us:
  Router/bridge/AP statistics pages (see example)
  Device status lights – Ethernet port
  Device connection port status page
Network Settings
  IP address (10.), netmask (optimal: 255.0.0.0), SSID, DHCP, Security
  AP/Auto/Bridge modes of the Dlink
Network Conflicts
  Duplicate IP addresses
  Mismatched frequency bands & wireless protocols- 2.4 or 5GHz, 802.11 a/b/g/n
  Security settings
  Noisy environment, e.g., several unrelated wireless networks conflicting with one another can produce temporary jerky robot responses
  Poor radio placement, e.g., near electronic noise or buried in metal frameworks

## Slide 19
LAN Statistics refer to the Ethernet connections
Wireless refers to the air traffic