## Slide 1: Power Transmission & Drivetrain

## Slide 2: Creating Effective Robot Mechanisms
Drivetrain: Moves Quickly Has Good Pushing Power (Power & Traction) Turns Easily Good Control
Manipulation: Picks up, Moves or Throws Game Pieces Consistently
Motors do not Overheat, Breakers do not Trip

## Slide 5
Basic Drive Train
Power Transmission & Drivetrain
Two Wheel Drive With Casters
Notes: Advantages? Disadvantages? Integrate wheel rotation sensors with any drive train! Helps especially during autonomous mode

## Slide 6
Basic Drive Train
Power Transmission & Drivetrain
Two Wheel Drive
All Traction Wheels
Notes: Advantages? Disadvantages?

## Slide 7
Basic Drive Train
Power Transmission & Drivetrain
Two Wheel Drive
Omniwheels on one Axle
Notes: Advantages? Disadvantages?

## Slide 8
Basic Drive Train
Power Transmission & Drivetrain
Four Wheel Drive
All Traction Wheels
Notes: Advantages? Disadvantages?

## Slide 9
Basic Drive Train
Power Transmission & Drivetrain
Four Wheel Drive
Omniwheels on one Axle
Notes: Advantages? Disadvantages?

## Slide 10
Drive Train
Power Transmission & Drivetrain
Six Wheel Drive
Notes: Advantages? Disadvantages? Note center wheels slightly lower. Why? Climbing?

## Slide 11
Drive Train
Power Transmission & Drivetrain
Four wheel Drive Super Traction Wheels All Wheels Steer
Turning Mode
Option:
Motor mounted shaft down with bevel gear drive
Notes: Advantages? Disadvantages Steering control can be done with chains, belts or steering motors and sensors

## Slide 12
Drive Train
Power Transmission & Drivetrain
Four wheel Drive Super Traction Wheels All Wheels Steer
Side Move Mode
Option:
Motor mounted shaft down with bevel gear drive
Notes: Advantages? Disadvantages?

## Slide 13
Mecanum Drive Train
Power Transmission & Drivetrain

## Slide 14
Transfer Power to another place
Reverse Direction of Input
Change Direction of Input
Change Motion Type
Increase Speed and Distance while decreasing torque
Decrease Speed and Distance while increasing torque
Power Transmission Possibilities

## Slide 15: Power Transmission Elements Levers
Class 1
Class 2
Class 3
Input
Output
Fulcrum
Input
Output
Fulcrum
Input
Output
Fulcrum
Give me a lever long enough and a fulcrum on which to place it, and I shall move the world.
Archimedes

## Slide 16: Power Transmission Elements Levers in Action
Input
Output
Fulcrum
Pneumatic Piston
50 Lbs Applied
4” Stroke
25 Lbs out
8” Stroke
What class Lever?
Note: connecting elements should be perpendicular at mid stroke!
Notes: What Class Lever?

## Slide 17: Power Transmission Elements Levers in Action
Input
Output
Fulcrum
Pneumatic Piston
50 Lbs Applied
4” Stroke
100 Lbs out
2” Stroke
Do Levers need to be Straight?
What class Lever?
Note: connecting elements should be perpendicular at mid stroke!
Notes: What Class Lever?

## Slide 18: Power Transmission Elements
Chains & Belts
Input
Output
Notes: Rotational Direction of Input and Output?

## Slide 19: Power Transmission Elements
Friction Drive
Gear Drive
Input
Output
Notes: Rotational Direction of Input and Output?

## Slide 20: Power Transmission Elements
Rotary Motion To Linear
Input
Rack & Pinion
Notes: Rotational Direction of Input and Output?

## Slide 21: Power Transmission Elements
Rotary Motion To Linear
Input
Ouput
Fulcrum
Notes: Rotational Direction of Input and Output?

## Slide 22: Power Transmission Elements
Calculating Ratios of a Powertrain
Input
Output
2 inches D
or
20 Teeth
3000 RPM
100 in/oz
Output element size
= Speed(RPM) & Distance Ratio
Input element size
Output element size
= Torque & Force Ratio
6 inches D
or
60 Teeth
Input element size
2
6
= .33 X 3000 = 1000 RPM out
6
2
= 3 X 100 = 300 in/oz out
Notes: Rotational Direction of Input and Output?

## Slide 23: Power Transmission Elements
Calculating Ratios of a Powertrain
Input
Output
2 inches D
or
20 Teeth
3000 RPM
100 in/oz
More than one ratio in a system? Multiply the individual ratios to find the overall ratio
6 inches D
2
6
= .0825 Speed Ratio X 3000 RPM= 247 RPM out
1” D
4” D
1
4
X
6
2
= 12 Torque Ratio X 100 in/oz= 1200 in/oz out
4
1
X

## Slide 24: Important Terms
Power Transmission Elements
Torque- The twisting or rotational force of a shaft (Driver or Driven)
Measured as a force applied a defined distance from the center of rotation
Examples:
Foot pound, Inch pound, inch ounce, newton meter
Distance 12 inches
Force 1 pound
Center of Rotation
1 Foot Pound

## Slide 25: Important Terms
Power Transmission Elements
RPM’s –Revolutions per minute
The Angular Velocity of an object- How fast is it turning?
Note: The CIM motor used for drive power on most robots turns at a about 5000 RPMs unloaded

## Slide 26: Important Terms
Power Transmission Elements
Power –(Horsepower) ability to do work
Always must include a force, a distance, and time
1 horsepower= lift 550 pounds one foot in one second
1 horsepower= 746 watts
Note: The Cim motor power ratings :
Voltage: 12 volt DC
No load RPM: 5,310 (+/- 10%)
Free Current: 2.7 amps
and 68 amps)
Stall Torque: 2.42 N-m, or 343.4 oz-in
Stall Current: 133 amps
Maximum Power: 337 Watts (at 2655 rpm, 172 oz-in)

## Slide 27: Power Transmission Elements
What You Need to Know
When Designing
1-Amount of load that needs to be moved? (Force)
2-How fast does it need to be moved ?(Time)
3- How far does it need to go? (Distance)
If this looks familiar, it is the power requirement of the task!
Notes: Rotational Direction of Input and Output?

## Slide 28: Power Transmission Elements
Common Mistake
Connecting a motor or piston to a mechanism without calculating the output force, distance and speed.
This has happened-more than once!
A CIM motor connected directly to a 6” Diameter Wheel
Speed of bot at 2655 CIM RPM --- 69 feet per second (FPS)
(Most bots have a maximum velocity of 10 FPS. Faster makes for a hard to control robot)
Load applied to ground at CIM 172 in/oz----2 pounds of force
(To drive a 130 pound robot)
Result-Bot does not move, breakers trip, magic white smoke?
Notes: Rotational Direction of Input and Output?

## Slide 29: Power Transmission Elements
Fisher-Price Gear Box Analysis
Input
R 550 motor
17,250 RPM .83 in/oz torque
Output
19
71
25
19
79
12
62
38
Wheel
Notes: Rotational Direction of Input and Output?

## Slide 30: Power Transmission Elements
Fisher-Price Gear Box Analysis
RPM (speed)
Input
R 550 motor
17,250 RPM .83 in/oz torque
Output
19
71
25
19
79
12
62
38
6” Wheel
19
71
X
25
79
19
62
12
38
X
X
=
.008
Speed Ratio
.008
X
17,200RPM
=
140 RPM Output
X 18” Wheel C = 2537 IPM /12=211fpm/60= 3.5 fps
Notes: Rotational Direction of Input and Output?

## Slide 31: Power Transmission Elements
Fisher-Price Gear Box Analysis
Torque
Input
R 550 motor
17,250 RPM .83 in/oz torque
Output
19
71
25
19
79
12
62
38
6”D Wheel
71
19
X
79
25
62
19
38
12
X
X
=
122
Torque Ratio
122
X
.83 in/oz
=
101 in oz output torque
/ 3” radius of wheel
=
34 oz at ground
Notes: Note at stall (0 RPM) motor torque is 70 in/oz

## Slide 32: Power Transmission Elements
Summary
Identify and research your available motors
Google search to find rated RPM and Torque, as well as power draw(Amps)
Design your mechanisms carefully
Calculate ratios and output distance, force applied, and time to actuate
NOTE: Match time is two minutes! A slow mechanism will reduce your performance
Always plan for adjustability. Adding extra fulcrum, input , and output attachment points is easier at the time initial manufacture
Always use double shear attachments when possible. They are much stronger and greatly improve the function of the mechanism
Single Shear
Double Shear
Notes: Note at stall (0 RPM) motor torque is 70 in/oz