## Slide 1
2012 Control System Changes
Version 3j
2/4/12

## Slide 2
Modules & breakouts
    But old module slot positions have changed
Programming-LV,C++,Java
  WPILib
    Slight modifications to make it easier to write portable code between the four and eight slot controllers
FPGA
    Model is new, but the FRC design circuit (hence behavior) will be the same for both cRIO FRC I&II
Powered for competition via the protected 24v output on the Power Distribution Panel
Warranty is 3-years from the NI ship date

## Slide 3
Hardware
  Half the slots (4)
  (1) each: analog/digital/solenoid module, plus one extra of the three
  4.4” shorter in length, same height & width
  ~two thirds the weight –new chassis alone is 1.42 lbs vs. original’s 2.05 lbs
  New conformal coating to minimize damage from metal dust and bits and pieces
Cost/Feature Optimized Between cRIO-9075 and cRIO-9076
  Processor-2x cache/memory bandwidth (2008 upgrade of the 2003 architecture)
  Increased Capability (Doubled from FRC I)
    Storage (512MB)
    System memory (256MB)
  No External DIP switches
    Same services performed by cRIO Imaging Tool or SAFE MODE via hold Reset button for 5 sec
  (1) Ethernet port – cameras get connected to and accessed from the DLink for processing
Power
  Two-wire connector (new one can fit the older cRIO, but old 4-wire does not fit new cRIO)
  9-30v (vs old 19-30v) operating voltage-24v recommended
  15W vs old 20W max power consumption (w/full set of the most power hungry modules)
  cRIO II has no internal battery to preserve the date/time during off state

## Slide 4
NI Software Installed
  Vision - Since the older cRIO has half the memory, and since the vision module has grown substantially in recent LabVIEW releases, the imaging tool installs a simplified version on the 8 slot.
    Smaller, stripped down, version of the Vision package (IMAQ) on the 8-slot
    The complete edition is installed on the 4-slot
    The features that were removed in the older cRIO FRC I were QR codes, meter reading, OCR, and other instrumentation and inspection features. Another beefy feature that we thought was not needed was the calibration.
cRIO Image Tool
  Still a single image zip will apply to both cRIO FRC I&II
  Will handle cRIO FRC I&II differences invisibly by extracting the appropriated files from the image zip
  Provide virtual DIP switch controls for cRIO FRC II
  Help validate modules are in the correct slots for both FRC I & FRC II

## Slide 5
OLD (2009-2011)-cRIO FRC I
NEW (2012)-cRIO FRC II
FRC cRIO Version Comparison | NEW FRC II (2012) | OLD FRC I (2009-2011)
 | cRIO 9075/9076 | cRIO 9072/9074
# slots | 4 | 6 (+2 unusable)
RS-232 | 1 | 1
Ethernet | 1 | 2
Dimensions-chassis | 7”(l) x 3.5”(w) x 2.5”(h) | 11.4”(l) x 3.5”(w) x 2.5”(h)
Weight-chassis | 1.42 lbs | 2.05 lbs
Operating Voltage | 9-30v | 19-30v
Power | 15W | 20W
System Memory | 256MB | 128MB
Storage Memory | 512MB | 256MB
Processor | Freescale MPC5125 | Freescale MPC5200
-data/instr cache | 32KB/32KB | 16KB/16KB
FPGA | Spartan-6 LX45 | Spartan-3 2000
-RAM | 2088 Kb | 720 Kb
-logic cells | 43,661 | 46,080
-multipliers | 58 | 40
-IO transfer rate | 1 Gb/s | 622 Mb/s
Note new slot configuration

## Slide 6
Teams can choose to use either cRIO FRC I or FRC II for the 2012 game
cRIO FRC II will not be useable until the 2012 Kickoff
Original cRIO FRC I no longer available for purchase after 9/30/11
    It will continue to be supported by NI tech support
New conformal coating means less damage from metal dust and fragments
Two slots lost = less potential capability
  But only affects maybe 5% of teams in one way or another
  Slots 1-3 on the cRIO FRC II are, in order, 1:Analog, 2:Digital, 3:Solenoid. Slot 4 on the cRIO FRC II will be a "wildcard" and one extra Analog, Digital, or Solenoid module may be used.
  For the 8-slot cRIO FRC I, slots 4 and 8 will now be unused. Slots 1-3 are in the same order as the cRIO FRC II, and Slots 5-7 are in the same order again (5: Analog, 6: Digital, 7: Solenoid). So you may have two of each type of module.
Smaller/Lighter = easier to place and meet weight
Increased memory/storage
  Not noticeable running standard user programs
  Better advantage of NI software (ease-of-use, additional services)
  Handle more complicated/efficient vision processing
  More room for on-board data logging
Power down to 9v = easier benchtesting NOT for competition
Troubleshooting steps change a little

## Slide 7
FRC teams that were registered for the 2011 season may use the 2011 discount right away.
Teams that register for the 2012 season may use the 2012 discount starting Oct 3, 2011. So, teams can use both the 2011 & 2012 allocation at one time.
Registered FRC teams get one Discount Credit each calendar year to purchase (Call NI at 1-866-511-6285 to order):
  The new cRIO FRC II kit (with 1 ea. 9201/9403/9472 modules) $525
  The new chassis only (no modules) $285
  (2) in any combination of both (1kit plus one chassis, 2 chassis-only, 2 kits) the items must be purchased in a single order
  Individual modules: analog/solenoid $152, digital $174
Teams may order additional cRIO FRC IIs at an educational price and individual modules at a slight discount.
The new cRIO FRC II may be ordered beginning Monday, Oct 3rd.
Initial deliveries will ship late November or early December.
Software for using/programming the new cRIO FRCII will not be available until kickoff. Beta teams will be testing this software starting in September.

## Slide 8
CAN
optional
CAN optional
Pit tethering
Both
FRC II
FRC I
Optional

## Slide 9
Optional 24v
Note new slot configuration

## Slide 10
Analog
  Inputs only
  Possible to use in lieu of digital inputs
Digital
  Inputs & Outputs
  PWM, Digital I/O, I2C, Relays
  Possible to use in lieu of solenoid outputs
Solenoid
  Outputs only
  Can power sensors via protected 24v source
  Possible to use in lieu of digital outputs
Module Tradeoffs

## Slide 11
Field Programmable Gate Array
    Huge collection of yes/no & sequential logic blocks in a massive routing grid
      Logic cells combine multiple inputs in boolean ways
      Flip-flops & registers are used for sequential logic
      All connected by reconfigurable wires via programmable switches
    Field Programmable just means the function of the board is defined by our program image, not when the hardware is made
    It trades custom chip efficiency (size, power, performance), e.g., cell phone, for adaptability and different cost factors, e.g., cell phone base stations
Where are FPGAs found around the house?
  Audio/Video (signal processing) - PC, TV, entertainment systems
  Automotive infotainment systems
  Wireless base stations keeping up with rapidly evolving cell phone features
NOT a computer processor like a Pentium or PowerPC
Sort of a generic reconfigurable custom digital (not analog) circuit
    Programming it is like doing a circuit design
    FRC uses it for super fast data input collection and output
    Teams do not touch it directly, only download updated FRC images

## Slide 12
The cRIO FRC II adds a protective conformal coating to the electronics helping to guard against metal dust and fragments that work their way into the case from shorting out the circuits.
The original cRIO FRC had user installable gaskets that many teams never used or even knew what they were for.

## Slide 13
Spec Links
cRIO-9074 (old) : http://sine.ni.com/nips/cds/view/p/lang/en/nid/203964
cRIO-9076 (new-similar) : http://sine.ni.com/nips/cds/view/p/lang/en/nid/209758
cRIO 9075/9076 Specs: http://www.ni.com/pdf/manuals/375650a.pdf
Comparison Tables: http://sine.ni.com/ds/app/doc/p/id/ds-204/lang/en
Freescale Processor Core:
  FRC II: http://cache.freescale.com/files/32bit/doc/ref_manual/e300coreRM.pdf
  FRC I: http://www.iuma.ulpgc.es/~nunez/clases-sed-mai-68ppc/powerpc_MPC603EUM.pdf
NJ Regional NI Survey of extra modules used
8% of teams (5) used an extra Digital module
3% of teams (2) used an extra Analog module
3% of teams (2) used an extra Solenoid module
*Photo credit for new cRIO FRC II- Arthur Dutra IV
Warranty on cRIO units are 3-years from the day the unit ships from NI.
NI FRC 2 cRIO FAQ: https://decibel.ni.com/content/docs/DOC-19103