2013 CRIO Robot:

As of 02/18/13

Analog Module 1:

- Winch pot

- Gyro

- Sled pot

- unused

- unused

- unused

- unused

- Battery

Digital Input/Output:

- Dumper Limit 1

- Dumper limit 2

- Shooter tach (Banner)

- Sled Limit 1

- Sled limit 2

- Mast limit1

- Mast limit2 (bumpers clear)

- Mast limit3

- unused

- unused

- unused

- unused

- unused

- unused

Relay Outputs:

- Dumper (Spike)

- unused

- unused

- unused

- unused

- unused

- unused

- unused

PWM:

- Left CIM motors (Y-cable, 2 Victors)

- Right CIM motors (Y-cable, 2 Victors)

- unused

- Winch motors (Y-cable, 2 Victors)

- Winch Pawl 1 (Servo)

- Winch Pawl 2 (Servo)

- Shooter (Victor)

- Sled (Talon)

- Top frisbee feeder (Servo)

- Bottom frisbee feeder (Servo)

Solenoid Output Module

N/A

Robot user switches:

N/A

Operator Interface:

- USB 1 - Joystick 1 – left tank

- Button 2 – Sled forward

- Button 3 – Sled backward

- USB 2 - Joystick 2 – right tank

- Button 2 – Sled forward

- Button 3 – Sled backward

- USB 3 – Xbox controller

- Right Joystick(axis 5) – Winch up/down (disabled when lock is engaged)

- Left Joystick(axis 2) – Dumper rotation

- Button A(1) – Shooter on

- Button B(2) – Shooter off

- Right trigger(axis 3) – fire frisbee

- Back button(7) – engage winch lock(winch disabled)

- Hold left bumper(5) + left trigger(axis 3) – disengage winch lock

Dashboard:

Sensor Feedback

- Winch pot

- Sled pot

- Dumper Limit 1

- Dumper Limit 2

- Sled limit 1

- Sled limit 2

- Shooter Tach

- Camera

Status

- Winch Locked (pawls engaged)

Autonomous:

- Do Nothing

- Dump

- Shoot

- Delay Auto

- Calibrate all speed controllers

- Sensor Validation

- Check limit switches

- Check all pots

- Check encoders

- Check gyro

- Check camera

Testing

- Direction of motors

- winch

- drive

- dumper

- shooter

- sled

- Servo angles

- winch pawl 1 -engaged/disengaged

- winch pawl 2 -engaged/disengaged

- Limit switch functionality

- Dumper front/back

- sled front/back

- winch top/bottom/middle

- Pot functionality & range

- Winch pot

- Sled pot